## Slide 1
WAll-e
An Autonomous Surveillance Robot
By Mohammad Thaher

## Slide 2
Abstract: The Vision of WAll-e
WAll-e is an autonomous obstacle-avoiding surveillance robot that utilizes a Raspberry Pi as its central processing unit. By integrating an HC-SR04 ultrasonic sensor with a servo motor, the robot can scan its surroundings to identify the safest path.
The system features advanced motor control techniques, including PWM-based pulsed motion and soft-start mechanisms, to ensure operational stability.
Furthermore, the robot enhances security by capturing images of detected obstacles and transmitting them to users via the Telegram platform.

## Slide 3
Introduction: Autonomous Surveillance
In modern applications such as safety monitoring and industrial inspection, autonomous mobile robots are becoming indispensable due to their ability to operate without constant human supervision.
Project Aim
The WAll-e project specifically addresses these needs by building a platform that integrates road traffic collision avoidance, object detection, and real-time observation using Python and the gpiozero library.

## Slide 4
Hardware Architecture
Processing & Power
Raspberry Pi: The central brain managing sensor data and actuator commands.
Power System: Three (3.7v) 18650 Lithium batteries provide portable, autonomous operation for the entire system.
Sensing & Actuation
HC-SR04 Sensor: Mounted on a servo for wide-angle environmental feedback.
L298N Module: High-current driver for precise control of two DC motors.

## Slide 5
Software Architecture: The Control Loop
01
Main Control Loop
The software operates as a continuous, infinite loop managing sensing, decision-making, and movement in real-time. It ensures the robot remains responsive to environmental changes.
02
Data Processing
To ensure reliability, the system employs a median filtering technique. It processes five consecutive distance readings to eliminate signal spikes and environmental noise.
Filter Logic
Rejects outliers to prevent false obstacle detection.
03
Decision Logic
The robot evaluates filtered data to decide between forward motion or an avoidance sequence: stopping, scanning 180°, and selecting the path with maximum clear distance.

## Slide 6
Control Algorithms: Precision and Stability
Motor Control
PWM Regulation
Pulse Width Modulation ensures precise
low-speed adjustments and smoother
motion.
Soft-Start Mechanism
Gradual acceleration reduces
mechanical stress and prevents sudden
jumps during startup.
Scanning Logic
Wide-Angle View
Servo-mounted sensors provide
environmental scanning across a broad
angular range.
Path Selection
The system identifies the path with the
maximum clear distance for optimal
navigation.
Safety Zones
Threshold Logic
Predefined distance zones (Critical, Slow,
Far) dictate immediate robotic
responses.
Real-Time Reaction
Continuous processing allows for
instantaneous adjustments to
environmental changes.

## Slide 7
Distance Zones & Logic
Zone
Distance Threshold
Robot Response
Critical
< 65 cm
Stop, scan surroundings, capture photo, and execute a turn.
Slow
65 – 145 cm
Enter caution mode with significantly reduced movement speed.
Far
> 145 cm
Maintain normal cruising speed and continue forward motion.
The robot's behavior is governed by these predefined thresholds to ensure safe navigation while optimizing operational efficiency in varying environments.

## Slide 8
Testing & Results: Validation
Sensor Accuracy
Median Filtering Success
Comprehensive testing confirmed that median filtering successfully stabilized sensor readings, effectively eliminating signal spikes and preventing unnecessary stops.
Navigation
Autonomous Path Selection
The robot consistently identified the optimal path during avoidance sequences and resumed its mission without manual intervention in all test cases.
Stability
Motion Precision
The transition to pulse-based PWM control and soft-start mechanisms significantly improved low-speed precision and reduced mechanical stress.
Communication
Telegram Alert Reliability
The alert system proved highly responsive, delivering captured images and status updates to the user with minimal latency and high reliability.

## Slide 9
Lessons Learned: Engineering Insights
Sensor Data Handling
Noise Management
Real-world sensor data is inherently
noisy. Robust filtering, such as the
median filter, is essential for reliable
decision-making.
Environmental Factors
Testing in diverse environments
highlighted the need for adaptable
thresholds to maintain consistent
performance.
Motion Control
Stability vs. Speed
Direct motor activation is jerky. Pulse-
based PWM control and soft-start
mechanisms are necessary for achieving
stable movement.
Mechanical Strain
Gradual acceleration not only improves
precision but also significantly reduces
mechanical wear on the robotic chassis.
Software Organization
Modular Architecture
Breaking the program into separate
functions for sensing, movement, and
alerts simplifies debugging and testing.
Error Handling
Integrating remote communication like
Telegram requires robust error handling
to prevent system crashes during
network issues.

## Slide 10
Future Enhancements: Scaling Up
Hardware Evolution
Advanced Sensing
Integration of RPLIDAR for 360-degree mapping and Arduino Uno for low-level task offloading to improve real-time response.
Intelligence & Vision
Object Classification
Implementing OpenCV and YOLOv5-tiny for real-time identification of people and objects in captured surveillance images.
System Architecture
Modular Framework
Transitioning to ROS2 (Robot Operating System) to create a scalable, modular architecture for complex multi-sensor missions.

## Slide 11
Conclusion: Project Impact
The WAll-e project successfully demonstrates the integration of real-time sensing, autonomous decision-making, and wireless communication in a mobile robotic platform.
It has provided invaluable hands-on experience in embedded systems and robotics engineering, serving as a robust foundation for future developments.
Key Achievement
WAll-e proves that intelligent control logic can transform simple hardware into a sophisticated autonomous system.
Project Completed Successfully